## Slide 1
COMPUTER COMMUNICATION NETWORKS
Department of Electronics and Communication Engineering

## Slide 2
COMPUTER COMMUNICATION NETWORKS
Department of Electronics and Communication Engineering
Unit 2 – Classes 42 & 46 – Numerical Problems for TCP

## Slide 3: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Graph 1
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 4: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Questions on Graph 1
A) Identify the intervals of time when TCP slow start is operating.
B) Identify the intervals of time when TCP congestion avoidance is operating.
Solution – Refer Graph 1 & Answer
Solution for A) TCP Slow start is operating in the intervals [1,6] and [23,26].
Solution for B) TCP Congestion avoidance is operating in the intervals [6,16] & [17,22].
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 5: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Graph 2
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 6: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Questions on Graph 2
C) After the 16th transmission round, is segment loss detected by a triple duplicate ACK or by a timeout?
Solution – Refer Graph 2 & Answer
Solution for C) After the 16th transmission round, packet loss is recognized by a triple duplicate ACK. If there was a timeout, the congestion window size would have been dropped to 1.
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 7: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Questions on Graph 2
D) After the 22nd transmission round, is the segment loss detected by a triple duplicate ACK or timeout?
Solution – Refer Graph 2 & Answer
Solution for D) After the 22nd transmission round, segment loss is detected due to timeout, and hence the congestion window size is set to 1.
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 8: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Graph 3
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 9: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Questions on Graph 3
E) What is the value of ssthresh at the first transmission round?
Solution – Refer Graph 3 & Answer
Solution for E) ssthresh is initially 32, since this is at this window size that slow start stops & congestion avoidance begins.
F) What is the value of ssthresh at the 18th transmission round?
Solution – Refer Graph 3 & Answer
Solution for F) threshold is set to half the value of cwnd when packet loss is detected. When the loss is detected during the transmission round 16, cwnd =42. Hence ssthresh = 21 in the 18th transmission round.
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 11: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Questions on Graph 4
G) What is the value of ssthresh at the 24th transmission round?
Solution – Refer Graph 4 & Answer
Solution for G) The threshold is set to half the value of the congestion window when packet loss is detected. When loss is detected during transmission round 22, the congestion windows size is 29. Hence the threshold is 14 (taking lower floor of 14.5) during the 24th transmission round.
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 13: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Questions on Graph 5
H) During what transmission round is the 70th segment sent?
Solution – Refer Graph 5 & Answer
Solution for H) During the 1st transmission round, packet 1 is sent; packet 2-3 are sent in the 2nd transmission round; packets 4-7 are sent in the 3rd transmission round; packets 8-15 are sent in the 4th transmission round; packets 16-31 are sent in the 5th transmission round; packets 32-63 are sent in the 6th transmission round; packets 64 – 96 are sent in the 7th transmission round. Thus packet 70 is sent in the 7th transmission round.
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 15: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Questions on Graph 6
I) Assuming a packet loss is detected after the 26th round by the receipt of a triple duplicate ACK, what will be the values of the congestion window size and of ssthresh?
Solution – Refer Graph 6 & Answer
Solution for I) The threshold will be set to half the current value of the congestion window (8) when the loss occurred and congestion window will be set to the new threshold value + 3 MSS . Thus the new values of the threshold and window will be 4 and 7 respectively.
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 17: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Questions on Graph 7
J) Suppose TCP Tahoe is used (instead of TCP Reno), and assume that triple duplicate ACKs are received at the 16th round. What are the ssthresh and the congestion window size at the 19th round?
Solution – Refer Graph 7 & Answer
Solution for J) Threshold is 21 and congestion window size is 1.
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 19: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Questions on Graph 8
K) Again suppose TCP Tahoe is used, and there is a timeout event at 22nd round. How many packets have been sent out from 17th round till 22nd round, inclusive?
Solution – Refer Graph 8 & Answer
Solution for K) round 17, 1 packet; round 18, 2 packets; round 19, 4 packets; round 20, 8 packets; round 21, 16 packets; round 22, 21 packets. So, the total number is 52.
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 20: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
-
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 21: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Consider the TCP graph shown in the previous slide. Assume TCP Reno Protocol & answer the following Questions
1) Which phase of the congestion control algorithm is happening between the transmission rounds 6 & 16 Justify ?
Solution – The Congestion Avoidance Phase happened between transmission rounds 6 & 16 because the congestion window increased by 1 MSS for each round
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 22: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
-
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 23: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Consider the TCP graph shown in the previous slide. Assume TCP Reno Protocol & answer the following Questions
2) How many TCP segments were transmitted between transmissions rounds 1 & 16 ?
Solution – Congestion Window (in MSS) increased as follows 1,2,4,8,16,32,33,34,35,36,37,38,39,40,41,42. Therefore, 438 segments were transmitted between rounds 1 & 16
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 24: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
C
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 25: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Consider the TCP graph shown in the previous slide. Assume TCP Reno Protocol & answer the following Questions
3) What happened in round 16? Justify.
Solution – The congestion window fell to cwnd = ssthresh+3 MSS (42/2+3 = 24 MSS) in round 17 because a triple duplicate ACK event occurred in round 16. ssthresh = cwnd/2
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 26: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
C
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 27: Unit 2 – Classes 42 & 46 – Numerical Problems for TCP
Consider the TCP graph shown in the previous slide. Assume TCP Reno Protocol & answer the following Questions
4) What happened in round 22? Justify.
Solution – A timeout event happened in round 22, therefore slowstart phase (cwnd = 1 MSS) commenced in round 23.
Notes: Packet loss occurs due to buffer overflow or corrupt packet or queue saturation at any intermediate router between the sender and the receiver. All these lead to timeout event. A corrupt packet is not a congestion event, however, as we can’t distinguish the causes of packet loss at the sender, we can simply assume that absence of an acknowledgement to a transmitted segment as network congestion.

## Slide 28
THANK YOU
Department of Electronics and Communication Engineering